CLS Florence GIII Bracket, Surface mounted fixture, black coated

| Type | : | 3 Watt IP40 surface mounted fixture, 360° rotatable, 270° tiltable, fitted with a cable of 150 cm |
| --- | --- | --- |
| Colour | : | Brushed aluminum black coated |
| Material | : | Anodized massive aluminum CNC cut heat sink |
| Weight | : | 45 gr |
| IP Rating | : | IP40 |
| IK class | : | X |
| Optics | : | Fitted with a 40° beam angle multi lens, possibility to change optics in 15° beam angle (supplied) |
| Light source | : | Cree high Power LED: 1 x |
| Colour Temperature | : | Warm white 3000K |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | External |
| Power factor driver | : | 1-10V driver >0,90 Phase cut driver >0,90, built-in active PFC |
| Dimming | : | 1-10V, phase cut, DMX 512, DALI or Bluetooth |
| Remarks | : | Extreme compact measurements |
| Optional accessories | : | X |
| Connection | : | Smart connect cabling system |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | European origin |

LED Lighting designed & made in The Netherlands since 2002