CLS Focus Compact zoom spot GII

| Type | : | 4 watt 13°-65° zoom spot |
| --- | --- | --- |
| Colour | : | Black |
| Material | : | Anodized aluminium |
| Weight | : | 135 gr |
| IP Rating | : | IP20 |
| IK class | : | x |
| Optics | : | 13°-65° zoom optics |
| Light source | : | Lumileds High Power LED: 1x Luxeon Z ES |
| Colour temperature | : | 2700K, 3000K, 4000K |
| CRI | : | ≈95 |
| Drive current | : | 700mA |
| Driver | : | External |
| Power factor driver | : | 1-10V > 90, Phase cut > 90 |
| Dimming | : | 1-10V, phase cut, DMX 512, DALI or Casambi |
| Remarks | : | Internal slot for correction filters |
| Optional accessories | : | Snoot, couplers, tilt extenders & extension pipes of 10 & 30 cm |
| Connection | : | Smart connect |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |