CLS HYLO Compact IP67 Up & Down lighter

| Type | : | 12 Watt IP67 Up & Down lighter |
| --- | --- | --- |
| Colour | : | Blank or black anodized aluminium |
| Material | : | Hard anodized CNC cut massive aluminium housing |
| Weight | : | 1600 gr |
| IP Rating | : | IP67 |
| IK class | : | 10 |
| Optics | : | Configurable: 8°, 12°, 30°, 61° & 12 x 46° beam angle. Possibility to have different beam angles for the up and down part |
| Light source | : | Lumileds High Power LED: 8 x Luxeon T |
| Colour temperature | : | 2700K, 3000K, 4000K, 5000K, 6500K, amber, blue, red & green LED colour is configurable for both up & down part of the fixture |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | 180-264 VAC driver built in |
| Power factor driver | : | >90 |
| Dimming | : | Not possible |
| Remarks | : | X |
| Optional accessories | : | X |
| Connection | : | 200 cm cable with open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands. |