CLS Jade Retail & Food Track spot

| Type | : | 20 Watt (2000 lm) or 30 Watt (3500 lm) track spot |
| --- | --- | --- |
| Colour | : | Configurable: Black, white or grey |
| Material | : | Anodized or coated aluminium & PC/ABS V0 |
| Weight | : | 780 gr |
| IP Rating | : | IP20 |
| IK class | : | x |
| Optics | : | Configurable: 19°, 37° or 63° beam angle |
| Light source | : | Citizen CoB LED module |
| LED Colours | : | Tuned for clothing, furniture, kitchens, jewellery, shoes, bread, meat, fish and vegetables & fruit Or 2500K, 2700K, 3000K, 4000K, 5000K |
| CRI | : | CRI>80 (single colour) or CRI>95 |
| Drive current | : | X |
| Driver | : | Internal power supply, 230V |
| Power factor | : | >0,90 |
| Dimming | : | Phase cut (mains dimmable) or local dim through potentiometer on housing |
| Remarks | : | Integrated soft diffusion filter |
| Optional accessories | : | Rail products |
| Connection | : | Track adapter |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |