CLS Jade Zoom Track spot

| Type | : | 25 Watt track zoom spot |
| --- | --- | --- |
| Colour | : | Configurable: Black, white or grey |
| Material | : | Anodized or coated aluminium & PC/ABS V0 |
| Weight | : | 952 gr |
| IP Rating | : | IP20 |
| Optics | : | Citizen: 9°- 58° Xicato: 11°- 67° |
| Light source | : | Citizen or Xitato LED module |
| Colour Temperature | : | 2700K, 3000K, 3500K & 4000K |
| CRI | : | Citizen: CRI>92 or CRI>97 Xicato: CRI>97 |
| Drive current | : | X |
| Driver | : | Internal power supply, 230V |
| Power factor | : | >0,90 |
| Dimming | : | Phase cut (mains dimmable), local dim, DALI, Bluetooth by Casambi, DMX512 or Wireless DMX. |
| Remarks | : | The beam angle can be adjusted easily from the backside of the fixture. So, one never has it hands in front of the light beam. |
| Optional accessories | : | Rail products. Customizable snoot. The snoot can be build up in segments of 2 cm, Rotatable barndoor, beam shapers & honeycomb Louvre |
| Connection | : | Track adapter, Global or Eutrac |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |

CLS Jade C Zoom semi built-up spot

| Type | : | 25 Watt semi built-up spot |
| --- | --- | --- |
| Colour | : | Configurable: Black, white or grey |
| Material | : | Anodized or coated aluminium & PC/ABS V0 |
| Weight | : | 952 gr |
| IP Rating | : | IP20 |
| Optics | : | Citizen: 9°- 58° Xicato: 11°- 67° |
| Light source | : | Citizen or Xitato LED module |
| Colour Temperature | : | 2700K, 3000K, 3500K & 4000K |
| CRI | : | Citizen: CRI>92 or CRI>97 Xicato: CRI>97 |
| Drive current | : | X |
| Driver | : | Internal power supply, 230V |
| Power factor | : | >0,90 |
| Dimming | : | Phase cut (mains dimmable), local dim, DALI, Bluetooth by Casambi, DMX512 or Wireless DMX. |
| Remarks | : | The beam angle can be adjusted easily from the backside of the fixture. So, one never has it hands in front of the light beam. |
| Optional accessories | : | Customizable snoot. The snoot can be build up in segments of 2 cm, Rotatable barndoor, beam shapers & honeycomb Louvre |
| Connection | : | 150 cm with shuko connector |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |

CLS Jade B Zoom semi built-up spot

| Type | : | 25 Watt semi built-up spot |
| --- | --- | --- |
| Colour | : | Configurable: Black, white or grey |
| Material | : | Anodized or coated aluminium & PC/ABS V0 |
| Weight | : | 952 gr |
| IP Rating | : | IP20 |
| Optics | : | Citizen: 9°- 58° Xicato: 11°- 67° |
| Light source | : | Citizen or Xitato LED module |
| Colour Temperature | : | 2700K, 3000K, 3500K & 4000K |
| CRI | : | Citizen: CRI>92 or CRI>97 Xicato: CRI>97 |
| Drive current | : | X |
| Driver | : | Internal power supply, 230V |
| Power factor | : | >0,90 |
| Dimming | : | Phase cut (mains dimmable), local dim, DALI, Bluetooth by Casambi, DMX512 or Wireless DMX. |
| Remarks | : | The beam angle can be adjusted easily from the backside of the fixture. So, one never has it hands in front of the light beam. Fitted with a M10 thread stud with cable entry. |
| Optional accessories | : | Customizable snoot. The snoot can be build up in segments of 2 cm, Rotatable barndoor, beam shapers & honeycomb Louvre |
| Connection | : | 150 cm open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |