CLS LON GII colour changing IP20 Down lighter

| Type | : | 10 Watt RGB + W or RGB + A direct DMX controlled IP20 colour changing down lighter |
| --- | --- | --- |
| Colour | : | Black coated aluminum |
| Material | : | Anodized massive aluminum CNC cut heat sink. PG 7 cable gland |
| Weight | : | 200 gr |
| IP Rating | : | IP20 |
| IK class | : | X |
| Optics | : | Fitted with a 25° beam angle multi lens, possibility to change optics in 40° beam angle |
| Light source | : | Lumileds: 4x Luxeon Rebel |
| Colour Temperature | : | RGB + W or RGB + A colour mixing |
| CRI | : | >85 |
| Drive current | : | 700mA |
| Driver | : | DMX driver intern, power supply external |
| Control | : | DMX 512 protocol |
| Dimming | : | DMX 512 protocol |
| Remarks | : | Totally uniform and even color mixing through patented mixing chamber Each unit is individually addressable and programmable Flange mounting system for installation in materials from 1mm to 25 mm |
| Optional accessories | : | MR16 fitting piece, 4-way RJ45-UTP distribution box, MR16 round or square Mounting plate |
| Connection | : | RJ45 in/output chassis connector |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |