CLS LON GII Bracket colour changing IP20 Surface Mounted fixture

| Type | : | 10 Watt RGB + W or RGB + A direct DMX controlled IP20 Surface mounted fixture |
| --- | --- | --- |
| Colour | : | Black coated aluminum |
| Material | : | Anodized aluminum CNC cut heat sink. |
| Weight | : | 250 gr |
| IP Rating | : | IP20 |
| IK class | : | X |
| Optics | : | Fitted with a 25° beam angle multi lens, possibility to change optics in 40° beam angle |
| LED | : | 4 x Luxeon Color Chips |
| Colour Temperature | : | RGB + W or RGB + A colour mixing |
| CRI | : | >85 |
| Drive current | : | 24 VDC |
| Driver | : | Power supply external |
| Control | : | DMX 512 protocol |
| Dimming | : | DMX 512 protocol |
| Remarks | : | Totally uniform and even color mixing through patented mixing chamber Each unit is individually addressable and programmable |
| Optional accessories | : | 4-way RJ45-UTP distribution box |
| Connection | : | RJ45 in/output chassis connector |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |