CLS Luxo 3 Basic CoB IP40 Downlighter

| Type | : | 10 Watt IP40 downlighter, 360° rotatable, 30° tiltable |
| --- | --- | --- |
| Colour | : | Housing available in anodized aluminium, black or white coated |
| Material | : | CNC machined aluminium heat sink. PG 7 cable gland |
| Weight | : | 220 gr |
| IP Rating | : | IP40 |
| IK class | : | X |
| Optics | : | Configurable: 28°, 37,5° or 62° beam angle |
| Light source | : | 1 x Cree CoB |
| Colour temperature | : | Extra warm white 2700K or warm white 3000K |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | External |
| Power factor driver | : | X |
| Dimming | : | 1-10V, phase cut, DMX 512 of DALI |
| Remarks | : | ‘Anti glare function by recessed light source |
| Optional accessories | : | X |
| Connection | : | SmartConnect cabling system |
| Life Time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | European origin |