CLS LUXO 3 RGB colour changing IP40 Down lighter

| Type | : | 7 Watt IP40 colour changing RGB down lighter, 360° rotatable, 40° tiltable, will be supplied as a light module complete with a removable mounting plate in either square or round shape |
| --- | --- | --- |
| Colour | : | Housing can be supplied in white, black or brushed aluminum |
| Material | : | Anodized massive aluminum CNC cut heat sink. PG 7 cable gland |
| Weight | : | 172 gr |
| IP Rating | : | IP40 |
| IK class | : | X |
| Optics | : | Fitted with a 40° beam angle multi lens, possibility to change optics in a 60° beam angle |
| Light source | : | Philips Lumileds: 3x Luxeon Rebel |
| Colour Temperature | : | RGB colour mixing |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | external |
| control | : | DMX 512 protocol |
| Dimming | : | DMX 512 |
| Remarks | : | Anti glare function by recessed light source |
| Optional accessories | : | Soft diffusion filter, round, square, 2 way rectangular, 3 way rectangular mounting plate. LDV-45 DMX driver |
| Connection | : | RJ45 loop trough |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | European origin |