See second page for IP52 version

CLS LUXO 6 Basic IP40 down lighter

| Type | : | 15,4 Watt IP40 down lighter, 360° rotatable, 40° tilt able Will be supplied with a non-dimmable driver |
| --- | --- | --- |
| Colour | : | Housing can be supplied in white coated, or brushed aluminum |
| Material | : | Anodized massive aluminum CNC machined heat sink. PG 7 cable gland |
| Weight | : | 510 gr |
| IP Rating | : | IP40 |
| IK class | : | X |
| Optics | : | Fitted with a 40° beam angle multi lens, possibility to change optics in 25°, 60° and 120° beam angle |
| Light source | : | Cree high Power LED’s: 6x |
| Colour Temperature | : | Extra warm white 2700K, warm white 3000K or neutral white 4000K |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | External |
| Power factor driver | : | 1-10V driver >0,90 Phase cut driver >0,90, built-in active PFC |
| Dimming | : | 1-10V or phase cut |
| Remarks | : | Anti glare function by recessed light source |
| Optional accessories | : | Soft diffusion filter, Phase cut driver, 1-10V driver |
| Connection | : | Smart connect cabling system |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | European origin |

CLS LUXO 6 Basic IP52 down lighter

| Type | : | 15,4 Watt IP52 down lighter, 360° rotatable, 40° tilt able Will be supplied with a non-dimmable driver |
| --- | --- | --- |
| Colour | : | Housing can be supplied in white coated, or brushed aluminum |
| Material | : | Anodized massive aluminum CNC machined heat sink. PG 7 cable gland |
| Weight | : | 510 gr |
| IP Rating | : | IP52 |
| IK class | : | X |
| Optics | : | Fitted with a 40° beam angle multi lens, possibility to change optics in 25°, 60° and 120° beam angle |
| Light source | : | Cree high Power LED’s: 6x |
| Colour Temperature | : | Extra warm white 2700K, warm white 3000K or neutral white 4000K |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | External |
| Power factor driver | : | 1-10V driver >0,90 Phase cut driver >0,90, built-in active PFC |
| Dimming | : | 1-10V or phase cut |
| Remarks | : | Anti glare function by recessed light source |
| Optional accessories | : | Soft diffusion filter, Phase cut driver, 1-10V driver |
| Connection | : | Smart connect cabling system |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | European origin |