CLS Mika Colour Flow & Tunable White series

| Type | : | 30 Watt rotatable & tilting colour changing downlighter, mountable in suspended ceilings. |
| --- | --- | --- |
| Colour | : | Housing available in black or white. |
| Housing | : | Black or white PS (PC_ABS V0), CNC cut housing of anodised aluminium. |
| Weight | : | 1325 gr |
| IP rating | : | IP20 |
| IK class | : | X |
| Beam angle | : | Configurable: 22°, 47° or 67° |
| LED | : | 1x CLS Dynamic Colour Chip |
| LED colours | : | RGBW, RGBA, 1800K-4000K or 2700K-5700K |
| CRI | : | Available on request |
| Driver Current | : | 100 ~ 240 VAC |
| Power factor | : | X |
| Control Methods | : | DMX 512 & Bluetooth by Casambi |
| Remarks | : | Delivery includes the CLS LDC-407 DMX LED driver with build in power supply. The Mika offers a 43º vertical adjustability. |
| Optional accessories | : | X |
| Life time | : | Up to 50.000 hour |
| Warranty | : | 3 years warranty |
| Origin | : | Designed & manufactured in The Netherlands |