CLS REVO Inground DMX-8

| Type | : | 20 Watt IP67 outdoor Inground mounted fixture |
| --- | --- | --- |
| Colour | : | Die cast housing + anti corrosion housing: black. Cover ring: stainless steel colour |
| Material | : | Marine grade 316 stainless steel mounting ring. Stainless steel 316 mounting screws. ABS plastic anti corrosion housing. Aluminum die cast housing |
| Weight | : | 6950 gr |
| IP Rating | : | IP67 |
| IK class | : | 10 |
| Optics | : | Configurable: 8°, 12°,30°,61°, 12 x 46° or 120° beam angle |
| Light source | : | Lumileds High Power LED: 8 x Luxeon T |
| Colour temperature | : | 2700K, 3000K, 5000K, 6500K, amber, blue, red & green |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | Internal 200 - 277 VAC IP67 power supply |
| Power factor driver | : | >0,90 |
| Dimming | : | DMX 512 control |
| Remarks | : | Ventilation gland with Gore-Tex membrane fitted to avoid moisture and condensation Fitted with a 5 core DMX combi cable Beam direction adjustable in multiple directions due to solid ball joint Double IP67 protection |
| Optional accessories | : | X |
| Connection | : | 200 cm cable with open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |