CLS REVO Basic Magno IP67 individually dimmable surface mounted outdoor fixture

| Type | : | 20 Watt IP67 outdoor fixture with Magno dimming |
| --- | --- | --- |
| Colour | : | Blank or black anodized aluminium |
| Material | : | Massive CNC machined aluminium |
| Weight | : | 1800 gr |
| IP Rating | : | IP67 |
| IK class | : | 10 |
| Optics | : | Configurable: 8°, 12°, 30°, 61°, 12 x 46° beam angle |
| Light source | : | Lumileds High Power LED: 8 x Luxeon T |
| Colour Temperature | : | 2400K, 2700K, 3000K, 4000K, 6500K, amber, blue, red, green |
| CRI | : | >80 |
| Driver current | : | 700mA |
| Driver | : | Internal: 100-240 VAC power supply |
| Control | : | Magno dimming |
| Dimming | : | Through Magno dim system |
| Remarks | : | Ventilation gland with Gore-Tex membrane fitted to avoid moisture and condensation Magno dimming offers the facility of individually dimmable IP67 fixtures without the need for any control equipment No extra cabling needed Calibration functionality |
| Optional accessories | : | Snoot, wall bracket, ground pin, extension pipe & magnet |
| Connection | : | 200 cm cable with open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |