CLS REVO Micro IP67 outdoor in ground mounted fixture

| Type | : | 5 Watt IP67 outdoor in ground mounted fixture |
| --- | --- | --- |
| Colour | : | Die cast housing + anti corrosion housing: black |
| Material | : | Marine grade 316 stainless steel mounting ring. Stainless steel 316 mounting screws. ABS plastic corrosion housing |
| Weight | : | 900 gr |
| IP Rating | : | IP67 |
| IK class | : | 10 |
| Optics | : | Configurable: 20°, 30°, 66° & 20 x 42° beam angle |
| Light source | : | Lumileds High Power LED: 4x Luxeon ZES |
| Colour temperature | : | 2700K, 3000K, 4000K & amber |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | 100-264VAC or 24V AC/DC built in |
| Power factor driver | : | >90 |
| Dimming | : | Not possible |
| Remarks | : | Ventilation gland with Gore-Tex membrane fitted to avoid moisture and condensation. IP67 2/3/4 way gel mold set included in the package |
| Optional accessories | : | X |
| Connection | : | 200 cm cable with open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |