CLS REVO Modular IP67 surface mounted outdoor fixture

| Type | : | 20 watt IP67 outdoor fixture with IP67 input/output connector for daisy chaining up to 25 units |
| --- | --- | --- |
| Colour | : | Blank or black anodized aluminium |
| Material | : | Massive CNC machined aluminium |
| Weight | : | 1800 gr |
| IP Rating | : | IP67 |
| IK class | : | X |
| Optics | : | Beam angle configurable: 8°, 12°, 30°, 61° or 12 x 46° beam angle |
| Light source | : | Lumileds High Power LED: 8 x Luxeon T |
| Colour Temperature | : | 2400K, 2700K, 3000K, 5000K, 6500K, amber, blue, red & green |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | 100- 240 VAC IP67 power supply built in |
| Power factor driver | : | >0,92 |
| Dimming | : | Not possible |
| Remarks | : | Ventilation gland with Gore-Tex membrane fitted to avoid moisture and condensation |
| Optional accessories | : | Snoot, wall bracket, ground pin, extension pipe |
| Connection | : | IP67 connector loop trough |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |