CLS REVO XL DUO DMX Colour Flow

| Type | : | 40 watt IP67 colour changing outdoor surface mounted fixture |
| --- | --- | --- |
| Colour | : | Blank or black anodized aluminium |
| Material | : | Massive CNC machined aluminium |
| Weight | : | 1800 gr |
| IP Rating | : | IP67 |
| IK class | : | X |
| Optics | : | Beam angle configurable: 8°, 12°, 30°, 61°, 80° or 12 x 46° beam angle |
| Light source | : | Lumileds High Power LED: 16 x Luxeon C /TX |
| Colour Temperature | : | RGBA, RGBW or AWB |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | Internal 100- 240 VAC IP67 power supply |
| Power factor driver | : | >0,99 |
| Control | : | DMX512 protocol |
| Remarks | : | Ventilation gland with Gore-Tex membrane fitted to avoid moisture and condensation. Fitted with a 5 core DMX combi cable. |
| Optional accessories | : | Snoot, wall bracket, ground pin, extension pipe |
| Connection | : | Cable with open end |
| Cable length | : | 200 centimeters |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |