CLS Ruby Bracket Modular

| Type | : | 110 Watt surface mounted spot |
| --- | --- | --- |
| Colour | : | Black or white, powder coated |
| Material | : | Aluminum |
| Weight | : | 3600 grams |
| IP Rating | : | IP20 |
| IK class | : | X |
| Reflector | : | Configurable: 16°, 49° or 63° beam angle |
| Light source | : | Citizen |
| LED Colour | : | 2700K, 3000K or 4000K |
| CRI | : | CRI>80 or CRI>92 |
| Driver | : | Internal, 80-264 VAC |
| Power factor driver | : | 1-10V driver >0,90 Phase cut driver >0,90, built-in active PFC |
| Dimming | : | DMX 512 protocol, PWM dimming, Full analogue dimming or Hybrid dimming |
| Remarks | : | Neutrik Powercon TRUE chassis / DMX XLR3 chassis |
| Optional accessories | : | Reflectors in several different beam angles and a Honeycomb louvre |
| Connection | : | Power: Neutrik Powercon TRUE DMX: XLR3 |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |
| Energy label | : | A+ & A++ |