CLS Ruby Bracket Modular Colour Flow

| Type | : | 110 Watt colour changing surface mounted spot |
| --- | --- | --- |
| Colour | : | Black or white, powder coated |
| Material | : | Aluminum |
| Weight | : | 3600 grams |
| IP Rating | : | IP20 |
| IK class | : | X |
| Reflector | : | Configurable: 16°, 49° or 63° beam angle |
| Light source | : | CLS Dynamic Colour COB |
| LED Colour | : | RGBW (W: 4000K) |
| Driver | : | Internal 80 ~ 264 VAC power supply |
| Control | : | DMX512 protocol, PWM dimming, Full analogue dimming or Hybrid dimming |
| Remarks | : | Neutrik Powercon TRUE chassis / DMX XLR3 chassis |
| Optional accessories | : | Reflectors in several different beam angles and a honeycomb louvre |
| Connection | : | Power: Neutrik Powercon TRUE DMX: XLR3 |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |
| Energy label | : | A+ |