CLS Ruby Compact Bracket Series

| Type | : | 30 Watt surface mounted spot |
| --- | --- | --- |
| Colour | : | Black or white, powder coated |
| Material | : | Aluminum |
| Weight | : | Various weights |
| IP Rating | : | IP20 |
| IK class | : | X |
| Reflector | : | Configurable: 19°, 37° or 63° beam angle |
| Light source | : | Citizen, Bridgelux, CLS Dynamic Colour Chip |
| LED Colour | : | 2500K, 2700K, 3000K, 3500K,4000K of 5000K |
| Colour Changing | : | RGBW (W:4000K) or RGBA |
| Tunable White | : | 1800K-4000K or 2700K-6500K |
| Dim To Warm | : | 1800K-3000K |
| CRI | : | CRI≈80 or CRI≈92 (white light versions) |
| Driver | : | Internal, 200-240 VAC |
| Power factor driver | : | 1-10V driver >0,90 Phase cut driver >0,90, built-in active PFC |
| Dimming | : | 1-10V, Mains Dim, DMX 512, DALI or Bluetooth by Casambi (white light version) |
| Control | : | PWM Dim, DMX Analogue dim or DMX Hybrid dim (colour changing version) |
| Remarks | : | X |
| Optional accessories | : | Honeycomb |
| Connection | : | 200 cm cable with open end |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 5 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |
| Energy label | : | A+ & A++ |