CLS Sapphire Zoom Track spot

| Type | : | 30 Watt track spot with an effective zoomrange of 8° till 60° |
| --- | --- | --- |
| Colour | : | Black, white, grey or a combination of colours |
| Material | : | Anodized aluminium & PC/ABS |
| Weight | : | 1600 gr |
| IP Rating | : | IP20 |
| IK class | : | x |
| Beam angle | : | Citizen Vivid: 8°- 50° Xicato: 8°- 60° |
| LED | : | Citizen or Xicato |
| Colour Temperature | : | 2700K, 3000K, & 4000K |
| CRI | : | Citizen Standard: CRI>92 Citizen Vivid: CRI>96 Xicato: CRI>98 |
| Power | : | 180 ~ 264 VAC |
| Driver | : | Internal power supply |
| Power factor | : | >0,91 |
| Dimming | : | Phase cut, via potentiometer on driver housing, DMX 512 or DALI |
| Remarks | : | Interchangeable Zhaga LED module Locking mechanisms for pan/tilt and zoom |
| Optional accessories | : | Barndoor & rail products |
| Connection | : | Track adapter |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in the Netherlands |