CLS Ultima Gallery spot

| Type | : | 20 Watt IP20 square track LED spot |
| --- | --- | --- |
| Colour | : | Black, grey, translucent, red, blue, green |
| Material | : | Anodized aluminium & PC/ABS V0 |
| Weight | : | 1,7 kg |
| IP Rating | : | IP20 |
| IK class | : | X |
| Optics | : | Configurable: 8°, 12°, 30°, 60° or 12 x 46° beam angle |
| Light source | : | Lumileds High Power LED: 16x Luxeon T |
| Colour temperature | : | 2700K, 3000K or 5000K |
| CRI | : | >80 |
| Drive current | : | 700mA |
| Driver | : | Internal power supply |
| Power factor | : | >90 |
| Dimming | : | Local Dim via potentiometer on driver housing |
| Remarks | : | UGR<13 |
| Optional accessories | : | Rail products |
| Connection | : | Track adapter |
| Life time | : | Up to 50.000 hours |
| Warranty | : | 3 years warranty |
| Origin | : | Designed and manufactured in The Netherlands |